## Slide 1: PANIMALAR INSTITUTE OF TECHNOLOGY
E.C.E
Assignment Date | 07 October 2022
Student Name | Madala Mourya
Student Roll Number | 211519106075
Maximum Marks | 2 Marks
Question:
Write python code for blinking LED and Traffic
lights for Raspberry pi.
CODE 1:
LED BLINKING
import RPi.GPIO as GPIO import time
GPIO.setmode(GPIO.BCM) cnt = 0
MAIL_CHECK_FREQ = 1
RED_LED = 4 GPIO.setup(RED_LED, GPIO.OUT)
while True:
if cnt == 0 :

## Slide 2
GPIO.output(RED_LED, False) cnt = 1
else:
GPIO.output(RED_LED, True) cnt = 0
time.sleep(MAIL_CHECK_FREQ) GPIO.cleanup()
CODE 2:
TRAFFIC LIGHTS FOR RASPBERRY PI
import RPi.GPIO as GPIO import time
try:
def lightTraffic(led1, led2, led3, delay ):
GPIO.output(led1, 1) time.sleep(delay)
GPIO.output(led1, 0)
GPIO.output(led2, 1)
time.sleep(delay) GPIO.output(led2, 0)
GPIO.output(led3, 1)
time.sleep(delay) GPIO.output(led3, 0) GPIO.setmode(GPIO.BCM) button = 19
GPIO.setup(button, GPIO.IN, pull_up_down=GPIO.PUD_UP) ledGreen = 16
ledYellow = 12

## Slide 3
ledRed = 23
GPIO.setup(ledGreen, GPIO.OUT) GPIO.setup(ledYellow, GPIO.OUT) GPIO.setup(ledRed, GPIO.OUT)
while True:
input_state = GPIO.input(button) if input_state == False: print('Button Pressed')
lightTraffic(ledGreen, ledYellow, ledRed, 1) else:
GPIO.output(ledGreen, 0)
GPIO.output(ledYellow, 0)
GPIO.output(ledRed, 0) except KeyboardInterrupt:
print ("You've exited the program")
finally:
GPIO.cleanup()